RADIATION SAFETY ANNUAL RESEARCH REFRESHER QUIZ

1.	The most common instrument for doing a laboratory radiation survey in a P-32 laboratory is the ____________.

A.	liquid scintillation counter

B.	Geiger-Mueller tube

C.	NaI detector

D.	Ion chamber

2.	The acronym ALARA describes a fundamental principle in radiation protection and stands for:

A.	As Long As Required To Achieve

B.	As Low As Reasonably Achievable

C.	As Low As Radioactively Available

D.	As Long As Radio Active

3.	The annual regulatory whole body exposure limit for a radiation worker is ________ mRem.

A.	500

B.	1000

C.	5000

D.	10000

4.	A pregnant radiation worker is required file a pregnancy declaration form.

A.	True

B.	False

5.	At GRU, an area is considered clean if a wipe survey shows removable contamination levels less than ________ dpm.

# A.	200

B.	500

C.	1000

D.	2000

6.	Radiation survey meters are calibrated ________.

- monthly

- quarterly

- semi-annually

- annually

7.	Laboratory contamination surveys are documented by laboratory personnel on a ________ basis

- weekly

- bi-weekly

- monthly

- quarterly

8.	The primary purpose of posting of radiological work areas is to:

- prevent workers from entering radiological areas

- inform workers of the radiological conditions and dangers

- allow EHS Radiation Safety personnel to measure the dose

- eliminate all occupational doses at GRU

9.	Swipe samples for tritium (H-3) contamination should be counted with a thin-window GM meter

- True

- False

10.	The three protective measures for reducing exposure are:

- time, dose and shielding

- dose, distance and shielding

- time, distance and shielding

- activity, dose and shielding

Tell us who you are:

Name:  __________________   _______________________

First                                  Last

Email: ___________________________________________

Dept: ____________________________________________

Phone: ___________________________________________

Name of Principle Authorized User (PAU):

___________________________________________

Comments:

______________________________________________________________________________

______________________________________________________________________________

# Text boxes

Submit